## Slide 1: Internet of Things
Water Quality Monitoring For Fish Cage
Bahar Barzegar
Salam Rishiraj Singh
Ali Shahrzad
April -2021

## Slide 2
Abstract
Water quality influences fish growth and survival rate. The purpose of this project is to monitor and control remotely water quality in real-time using IOT technology through sensors and actuators connected to the internet (or cloud service).
Objective
Our goal is to develop a small, relatively inexpensive, portable device that can be deployed in offshore for real-time water quality monitoring that could potentially reduce time-consuming daily visits to the offshore fish cage.
Users
Fish farming operators

## Slide 3: Questions
What is the problem and why do you need IoT?
The problem is water quality monitoring of Offshore Fish Cages. Most of the fish cages are located miles away in the offshore, which daily monitoring in presence of operators will be expensive and time consuming. Scientists and operators need a way to observe water quality, fish feeding habit and growth on a regular basis without having to visit the cages themselves. Eventually the control of offshore operations should be done remotely. Remote monitoring can be done using IoT that uses sensors and actuators connected to internet and we can monitor and control Fish cages, using web-based applications serviced by cloud based IoT platform.

## Slide 4
2. What are the connected components, the protocols to connect them and the overall IoT architecture?
Connected Components are illustrated in the following structure:

## Slide 5: IoT Architecture

## Slide 6
3. What data are collected and by which sensors?
Waterproof DS18B20 Digital temperature Sensor |  | Analog Data- (Celsius)
Analog Turbidity Sensor Presence of solid particles |  | Analog Data - (Volt)
Analog pH Sensor Acidity of water |  | Analog Data– Acidity(pH)

## Slide 7
4. What kind of collective intelligence do you expect will emerge?
Water Purity – Water Pollution
Based on the value of Turbidity and pH sensors, we have the knowledge to know whether the water is polluted or not. Also by using Temperature sensor, we can have water temperature data.
Water Pump status
Based on the value of Turbidity and pH sensors, a Water pump will be turned on/off to add pure water to change the water purity. Therefore, we can have a status indication for water pump beside water characteristics.
Statistics data
Based on historical data (Trend values) we can have an estimation of the time duration which we have the most water pollution or impurity.

## Slide 8
5. What are you going to learn and how will you act into the environment by what actuators?
We are going to monitor three important parameters of water in fish-living area to monitor and control the fish growth and prevent fish death.
In case of water impurity, which can be measured by pH and Turbidity sensors, we will start a water pump to add pure water to the Fish Cage to make the water pure in comparison with previous state.
In case of water high temperature, we will turn on an LED to notify operators to start pump to add some cold water to the existing Fish cage.

## Slide 9
6. How are you going to measure the effectiveness of your actions into the environment?
Water pollution is one of the biggest issue affecting the fish growth and survival rate. In order to guarantee clean water for fish cages, it should be based on real-time monitoring. In this project, we present a design and development of a low cost system for real time monitoring of the water quality. The system measures physical and chemical parameters of the water. The parameters such as temperature, PH, turbidity of the water can be measured. These values will interpret by Data processing part of the system (Controller) and relevant actions will be applied to the environment through actuators at the right time. Therefore having a real time sensing and actuation will be effective and prevent fish death in our case.

## Slide 10
7. What are the constraints? How often? Bandwidth? Latency? Energy? Duty Cycle?
In our proposed solution, mainly we are going to face power and network limitations. As we are using multiple sensors, actuators, Wi-Fi module and development board, we need a stable power connection, in case of using a battery, it can lead us for less power consumption. On the other hand, if we lose our network connection it can create a latency to update system instantly.
8. What is the plan and what are the metrics (quantitative, not qualitative) to evaluate the performance.
To measure the performance of our proposed system we are going to test our device and its components with exciting solutions which are already available in the market to verifies our result’s accuracy. Once our device will be fully functional we will run different scenarios to compare our device results with existing results to find out the performance . There are many tools available in the market to evaluate the IOT devices performance for example JTAG Dongle , Wireshark and Shodan etc. .